## Slide 1: Permiting
UCF Building Department

## Slide 2: When are permits required?
[A] 105.1 Required. Any owner or owner’s authorized agent
who intends to construct, enlarge, alter, repair, move, demolish
or change the occupancy of a building or structure, or to
erect, install, enlarge, alter, repair, remove, convert or
replace any impact-resistant coverings, electrical, gas,
mechanical or plumbing system, the installation of which is
regulated by this code, or to cause any such work to be performed,
shall first make application to the building official
and obtain the required permit.

## Slide 3
[A] 105.2 Work exempt from permit. Exemptions from
permit requirements of this code shall not be deemed to grant
authorization for any work to be done in any manner in violation
of the provisions of this code. Permits shall not be
required for the following:
There are no permit exemptions for Building or Electrical under the Florida Building Code. Only Mechanical, Gas and Plumbing have exemptions. UCF has specific exemptions for Electrical

## Slide 4
Gas:
1. Portable heating appliance.
2. Replacement of any minor part that does not alter
approval of equipment or make such equipment
unsafe.

## Slide 5
Mechanical:
1. Portable heating appliance.
2. Portable ventilation equipment.
3. Portable cooling unit.
4. Steam, hot or chilled water piping within any heating
or cooling equipment regulated by this code.
5. Replacement of any part that does not alter its
approval or make it unsafe.
6. Portable evaporative cooler.
7. Self-contained refrigeration system containing 10
pounds (4.54 kg) or less of refrigerant and actuated
by motors of 1 horsepower (0.75 kW) or less.
8. The installation, replacement, removal or metering
of any load management control device.

## Slide 6
Plumbing:
1. The stopping of leaks in drains, water, soil, waste or
vent pipe, provided, however, that if any concealed
trap, drain pipe, water, soil, waste or vent pipe
becomes defective and it becomes necessary to
remove and replace the same with new material,
such work shall be considered as new work and a
permit shall be obtained and inspection made as provided
in this code.
2. The clearing of stoppages or the repairing of leaks in
pipes, valves or fixtures and the removal and reinstallation
of water closets, provided such repairs do not involve or
require the replacement or rearrangement
of valves, pipes or fixtures

## Slide 7
UCF Permit Exemptions
Electrical:
Replacing switches, outlets or breakers of the same type and size.

## Slide 8
[A] 105.2.1 Emergency repairs. Where equipment
replacements and repairs must be performed in an emergency situation, the permit application shall be submitted within the next working business day to the building official.

## Slide 9
“Conditional Start”
105.12 Work starting before permit issuance. Upon
approval of the building official, the scope of work delineated
in the building permit application and plan may be started
prior to the final approval and issuance of the permit, provided
any work completed is entirely at risk of the permit
applicant and the work does not proceed past the first
required inspection.
A conditional start can be requested by email, with your Director cc’d on your request.

## Slide 10
All contractors performing work must be licensed.
State Employees can perform work up to $200,000 per FL SS 489.103 Exemptions:
(3) An authorized employee of the United States, this state, or any municipality, county, irrigation district, reclamation district, or any other municipal or political subdivision, except school boards, state university boards of trustees, and community college boards of trustees, unless for the purpose of performing routine maintenance or repair or construction not exceeding $200,000 to existing installations, if the employee does not hold himself or herself out for hire or otherwise engage in contracting except in accordance with his or her employment. If the construction, remodeling, or improvement exceeds $200,000, school boards, state university boards of trustees, and community college boards of trustees shall not divide the project into separate components for the purpose of evading this section.

## Slide 11: Engineering Requirements: 105.3.1.2 No permit may be issued for any building construction, erection, alteration, modification, repair, or addition unless the applicant for such permit provides to the enforcing agency which issues the permit any of the following documents which apply to the construction for which the permit is to be issued and which shall be prepared by or under the direction of an engineer registered under Chapter 471, Florida Statutes:

## Slide 12
1. Plumbing documents for any new building or
addition which requires a plumbing system with
more than 250 fixture units or which costs more
than $125,000.
2. Fire sprinkler documents for any new building or
addition which includes a fire sprinkler system
which contains 50 or more sprinkler heads. Personnel
as authorized by chapter 633 Florida Statutes,
may design a fire sprinkler system of 49 or
fewer heads and may design the alteration of an
existing fire sprinkler system if the alteration
consists of the relocation, addition or deletion of
not more than 49 heads, notwithstanding the size
of the existing fire sprinkler system.

## Slide 13
3. Heating, ventilation, and air-conditioning documents
for any new building or addition which
requires more than a 15-ton-per-system capacity
which is designed to accommodate 100 or more
persons or for which the system costs more than
$125,000. This paragraph does not include any
document for the replacement or repair of an
existing system in which the work does not
require altering a structural part of the building or
for work on a residential one-, two-, three-, or
Four-family structure.*

## Slide 14
An air-conditioning system may be designed
by an installing air-conditioning contractor certified
under Chapter 489, Florida Statutes, to serve
any building or addition which is designed to
accommodate fewer than 100 persons and
requires an air-conditioning system with a value
of $125,000 or less; and when a 15-ton-per system
or less is designed for a singular space of a
building and each 15-ton system or less has an
independent duct system. Systems not complying
with the above require design documents that are
to be sealed by a professional engineer.

## Slide 15
4. Any specialized mechanical, electrical, or plumbing
document for any new building or addition
which includes a medical gas, oxygen, steam,
vacuum, toxic air filtration, halon, or fire detection
and alarm system which costs more than
$5,000.

## Slide 16
5. Electrical documents. See Florida Statutes 471.003(2)(h).
Documents requiring an engineer seal by this
part shall not be valid unless a professional engineer
who possesses a valid certificate of registration
has signed, dated, and stamped such
document as provided in Section 471.025, Florida Statutes.
6. All public swimming pools and public bathing
places defined by and regulated under Chapter
514, Florida Statutes.

## Slide 17: Engineering 471.003 Qualifications for practice; exemptions
(b) 1. A person acting as a public officer employed by any state, county, municipal, or other governmental unit of this state when working on any project the total estimated cost of which is $10,000 or less.
2. Persons who are employees of any state, county, municipal, or other governmental unit of this state and who are the subordinates of a person in responsible charge licensed under this chapter, to the extent that the supervision meets standards adopted by rule of the board.
(h) Any electrical, plumbing, air-conditioning, or mechanical contractor whose practice includes the design and fabrication of electrical, plumbing, air-conditioning, or mechanical systems, respectively, which she or he installs by virtue of a license issued under chapter 489, under former part I of chapter 553, Florida Statutes 2001, or under any special act or ordinance when working on any construction project which:
1. Requires an electrical or plumbing or air-conditioning and refrigeration system with a value of $125,000 or less; and
2.a. Requires an aggregate service capacity of 600 amperes (240 volts) or less on a residential electrical system or 800 amperes (240 volts) or less on a commercial or industrial electrical system;
b. Requires a plumbing system with fewer than 250 fixture units; or
c. Requires a heating, ventilation, and air-conditioning system not to exceed a 15-ton-per-system capacity, or if the project is designed to accommodate 100 or fewer persons.